## Slide 1
Ch. 5
Introduction to Circuits

## Slide 2: Material Classification
Conductor : a material in which charges can move to neighboring atoms with relative ease
E.g.
Insulator: a material that opposes the charge movement (i.e. No charge movement)
E.g.

## Slide 3: Material Classification
Semi - conductor : a material whose conductive properties are somewhat in between those of conductor and insulator
E.g. Silicon

## Slide 4: Electrical Current
Current = The time rate of flow of electrical charge through a conductor or circuit element.
Unit: Amperes (A) = Coulombs per second (C/s)
Depends on
Cross-section area
No. of charge passing through the area

## Slide 5: Waterfall analogy to current
Current represents how much water going over the edge of the falls each second
Larger
Smaller

## Slide 6: Direct and Alternating Currents
Direct Current (d.c.):
When a current is constant with time
Alternating Current (a.c.):
When a current is varying with time, reversing direction periodically
Current

## Slide 7: Voltage
A measure of the energy available (potential) per unit of charge when charge moves from one point to other point in an electrical circuit.
Unit: Volt (V) = Joules per coulomb (J/C)
The voltage Vab has a reference polarity that is positive at point a and negative at point b.

## Slide 8: Waterfall analogy to voltage
The higher the voltage, the higher the waterfall
Source: http://sargosis.com/articles/science/intro-guide/basic-electric-concepts/

## Slide 9: Resistors and Resistances
Resistance :
  Different material allows charges to move within them with different levels of ease. The physical property or ability to resist current.
  Is a cirvuit property for which voltage is proportional to current
Resistor :
  Is a two-terminal device composed of a conductive material.

## Slide 10: Resistors and Resistances
Resistance of commercial electric wires :
  The thicker the wire, the more cross sectional area for the current to flow through, so the smaller the resistance
  A so-called No. 4 wire 100 ft long has a resistance of 0.025 Ω , whereas the same length of No. 10 wire, which is thinner, has a resistance of 0.1 Ω.

## Slide 11: Ohm’s Law
The voltage V across an ideal resistor is proportional to the current I through the resistor. The constant of proportionality is the resistance R.
V = IR

## Slide 12: Power and Energy
Current I is the rate of flow of charge and voltage V is the measure of energy transferred per unit of charge, the product of the current and voltage is power P (i.e. the rate of work)
Note that power is always positive, not a function of the direction of current flow
The total amount of energy generated over a period of time (in unit of kilowatt-hr) is the work done (or energy use). This is what is charged in an electric bill.
P = V x I = I2/R Unit: Watt (W)

## Slide 13: Quiz 1
What’s the current passing through the resistor?
What’s the power of the circuit?
V = IR

## Slide 14: Quiz 1
What’s the current passing through the resistor? (Ans: 0.9A)
What’s the power of the circuit? (Ans: 8.1W)
V = IR
P = VI

## Slide 15: Quiz 1a
If 80 A flows through 100 ft of No. 4 wire, what is the voltage loss ?
What is the corresponding voltage loss for a No. 10 wire ?

## Slide 16: Quiz 1a
If 80 A flows through 100 ft of No. 4 wire, what is the voltage loss ? (2V)
What is the corresponding voltage loss for a No. 10 wire ? (8V)
Note: the cost is different for the two wires, one 100 ft length of insulated No. 4 wire would cost about $120, whereas 100 ft of insulated No. 10 wires would cost about $23. (prices at yr 2000)

## Slide 17: Concept of Fuse
Electricity supply from the grid provide individual home with outlet of 120 V
Fuse are provided to limit the amount of current flow through one circuit
For a home uses 15A fuses, then the total current in one circuit must be less than 15A.
Example: a 60 W light bulb uses 0.5 A, so the number of 60 W light bulbs which can be powered from a 15A circuit is 30.

## Slide 18: Series circuit
Resistors are in one line
Current is identical at every point
Rtotal = R1 + R2 + ….+ Rn
Iin = Iout

## Slide 19: Parallel circuit
Resistors are in parallel
Voltage of every branch is the same
V = V1 = V2 = … = Vn
Rtotal = (R1-1 + R2-1 + ... + Rn-1) -1

## Slide 20: Example
Source: David Irwin, Mark Nelms (2008), Basic Engineering Circuit Analysis (9 edition),

## Slide 21: Voltage Division
Source: David Irwin, Mark Nelms (2008), Basic Engineering Circuit Analysis (9 edition),

## Slide 22: Current Division
Source: David Irwin, Mark Nelms (2008), Basic Engineering Circuit Analysis (9 edition),

## Slide 23: Quiz 2
What are the values for following items:
RT, IT, IR1, IR2, IR3, VR1, VR2, VR3

## Slide 24: Quiz 2 (Ans)
RT = 10 k ohm
IT = 1mA
IR1 = 1mA
IR2 = 0.33mA
IR3 = 0.67mA
VR1 = 6V
VR2 = 4V
VR3 = 4V

## Slide 25: Discussion
Both series and parallel circuit can be applied to lighting, what are the advantages and disadvantages?

## Slide 26: Discussion
Both series and parallel circuit can be applied to lighting, what are the advantages and disadvantages?
 | Parallel | Series
Advantages | One light goes out but others don’t go out It is used in houses | Don’t overheat easily
Disadvantages | Uses lots of wires | If one light bulb goes out, others go out as well

## Slide 27: Open Circuit
Open Circuit:
  The circuit is open, no current flows on the opened line
  This is equivalent to connect an infinite large resistor connected to the circuit

## Slide 28: Short Circuit
Short Circuit:
  Connect two points of a resistor with a wire
  The wire has a very near to zero resistance
  Short circuit is equivalent to connect two points of a circuit element with a infinitely small resistor
Short circuit could damage the circuit components.

## Slide 29: Recap
Voltage, Current, Resistance
Ohm’s Law I=V/R
Series: current is the same
Parallel: Voltage is the same
Open circuit: infinitely large resistance
Short circuit: infinitely small resistance