## Slide 1: Design for Appropriate Technology

## Slide 2: The Design Process

## Slide 3: The Design Process

## Slide 4: The Design Process
The first step – Ask questions
  To clarify problem so the designers can know what solutions are reasonable
  Designers bring their own experience, culture, training and personality in the development of an initial concept for the design

## Slide 5: The Rwanda System

## Slide 6: The Rwanda System

## Slide 7: The Rwanda System
The first step – Ask questions
    To clarify problem so the designers can know what solutions are reasonable
  The poverty in Rwanda
    clean water and energy are both needed
    Water is semi-accessible with a great deal of cost of time and labor
    No access to electrical grid for at least 10 years in some region
  The objective is to provide electricity to the Rwanda village
    How much electricity (the size of the system)
      Small scale to address basic needs, sufficient to provide lights and charging of devices (radio, flashlights, cell phones)
      Will not design for electricity supply for air conditioning, refrigeration etc. (no AC/DC conversion, less complexity and also not immediate needs)

## Slide 8: The Rwanda System
The first step – Ask questions
  Designers bring their own experience, culture, training and personality in the development of an initial concept for the design
    Use solar energy
      Sun is readily available in village
      Minimum impact to their ways of life
      Price of solar cells/panels is low
      LED light bulb is cheap, circuit design not difficult

## Slide 9: The Design Process
The second step – testing
  General criteria most designs must meet to be viable
    Effectiveness
    Reliability
    Maintainability
    Reparability
    Availability

## Slide 10: The Design Process
The second step – testing
  General criteria most designs must meet to be viable
    Effectiveness
      The concept must meet the requirements, e.g.
      a self sufficient farm must produce enough food to feed its inhabitants

## Slide 11: The Rwanda System
The second step – testing
  General criteria most designs must meet to be viable
    Effectiveness
      Solar/electricity technology is mature, should provide the intended amount of power
      Power were sufficient to provide up to 3~4 LED lights in different rooms
      LED light was of sufficient brightness
      Sufficient power to charge cell phone or rechargeable batteries

## Slide 12: The Design Process
The second step – testing
  General criteria most designs must meet to be viable
    Reliability
      A reliable product performed as design when called upon
      All product fails due to uncontrolled factors, e.g. A bicycle system might fail on snowy days. Some cars do not start on cold mornings
      Measures of reliability are frequency of repairs and mean time before fails

## Slide 13: The Rwanda System
The second step – testing
  General criteria most designs must meet to be viable
    Reliability
      All components (solar panel, convertor, batteries, LED lights) are known to be durable and reliable
      Major problems (e.g. mechanical damage or dust accumulation on solar panel, wetting battery on rainy days can be avoided with good operational practice)
      The main source of failure is in the connection between component (e.g. wiring) and can be dealt with by maintenance

## Slide 14: The Design Process
The second step – testing
  General criteria most designs must meet to be viable
    Maintainability
      All devices need maintenance or upkeep
      A good design would allow the user or service person to perform routine maintenance easily and safely
        Auto engine compartment is designed with easy access to the spark plugs
        A village water pump is designed with the seals accessible with common hand tools

## Slide 15: The Rwanda System
The second step – testing
  General criteria most designs must meet to be viable
    Maintainability
      Connection issues can be addressed with simple engineering skill
        Replacing electrical wire with simple soldering
        Understand simple electrical circuit to trouble shoot
        Simple mechanical concept to repair stands

## Slide 16: The Design Process
The second step – testing
  General criteria most designs must meet to be viable
    Reparability
      When product fails (as it always will), the failed part should be replaceable and the effort to replace it should take only a reasonable amount of time and effort
      A key argument for Appropriate Technology, as many imported machines in developing countries stand idle because the parts needed for repairs are not there

## Slide 17: The Rwanda System
The second step – testing
  General criteria most designs must meet to be viable
    Reparability
      Components (solar panel, controller, batteries, LED light bulb) are available locally at Rwanda
      The price is lower if they can be ordered directly from oversea (e.g. China)

## Slide 18: The Design Process
The second step – testing
  General criteria most designs must meet to be viable
    Availability
      The device should be functional when you need it
      Design must deal with the availability of energy source (if energy is needed for the running of the device, e.g. the availability of the sun in the operation of a solar oven)

## Slide 19: The Rwanda System
The second step – testing
  General criteria most designs must meet to be viable
    Availability
      System should work when sunlight is available
      Operate independently with no oversight required

## Slide 20: The Design Process
The third step – preliminary design and evaluation
  If the concept passes the test, a preliminary design is made and again evaluated
  The evaluation asks two kinds of questions of the preliminary designs
    Hardware Related
    Software Related

## Slide 21: The Design Process
The third step – preliminary design and evaluation
  Hardware Related Evaluation
    What is the worst case combination of high demand and low availability and how would the design perform in the worst case ?
    Is the necessary material available ?
    Is the labor for construction available ?
    What is the monetary cost ?
    Is the construction time reasonable ?

## Slide 22: The Rwanda System
The third step – preliminary design and evaluation
  Hardware Related Evaluation
    The system is available to function even when the sun is not available (for the short term) because of the battery
    Some unique challenge in doing AT in a foreign country
      Implementation must occur over a short period of time (1~2 week)
      Hardware must be available (components are small enough that most can be bought oversea to reduce cost)
      Construction happens locally (must run through the construction process thoroughly at home, prior to the trip)
      Manuel hand-on skills are necessary for last minute, unexpected change required for the design

## Slide 23: The Design Process
The third step – preliminary design and evaluation
  Software Related Evaluation
    This evaluation deals with the “soft costs”, those hard to put a number on
      What is the environmental impact ?
      What is the effect on the user’s lifestyle ?
      Does the design exclude any potential user ?
      Does it provide a path to adapting the changing needs ?

## Slide 24: The Rwanda System
The third step – preliminary design and evaluation
  Software Related Evaluation
    This evaluation deals with the “soft costs”, those hard to put a number on
      No direct environmental issues with the system as it has no impact to the environment
      But there are issue with deciding placement of the solar panel on the roof .vs. the selected mobile ground design (for security reason and also easy sharing with neighbors)
      Impact of lifestyle is significant (life now continues after sunset!!, no two-hour round trip down the hill to charge cell phone!!!)
      Design is sufficiently simple to encourage additional users to build system on their own
      Can look to expand system in the future to meet other more advance electricity needs

## Slide 25: The Design Process
The third step – preliminary design and evaluation
  Failure of a preliminary design is not fatal since the design can be modified and improved
  A single design is almost never best in all regards; a short construction time, for example, may mean a high cost. The designer must make trade-offs

## Slide 26: The Design Process
The fourth step – the construction of a prototype and making a production
  Details are important, every nuts and bolts must be specified
  Design decision must be made ahead of time
    The design must be communicated to the craftpeople who will execute the design based on drawing, numbers and words
    The detail process may bring to light subtle flaws. Some design decisions must be made on the field, i.e., during the actual construction
    Since it is almost impossible to forsee and design for every contingency, the prototype gives the designer one more chance to test the concept before committing it to production

## Slide 27: The Rwanda System
The fourth step – the construction and installation on site
  Details are important, every nuts and bolts must be specified
    Documentation of the construction process is very important, as we want to pass all the detailed knowledge to the villagers who have little education
  Design decision must be made ahead of time
    Took pictures of the house to understand the condition for installation of LED lights
    Basic engineering skills are important as you always need to make last minute change due to the situation

## Slide 28: Major Points about Design
Design is an iterative process
  One might need to go around the loops many time until a concept, preliminary design, or detailed design is satisfactory
It is better to spend much time working on the original concept than to try to salvage a poor idea in the final phases
  As a design proceeds it becomes more difficult to reject its basic concept and start again. The investment of time, energy, psyche, and capital give a well along design too great a value to be dropped.
Trade-offs must be made to get some semblance of the initial concept into production
  An “ideal” solution rarely sees the light of day. There are too many competing constraints

## Slide 29: Major Points about the Rwanda System
Design is an iterative process
  One might need to go around the loops many time until a concept, preliminary design, or detailed design is satisfactory
It is better to spend much time working on the original concept than to try to salvage a poor idea in the final phases
  Spend as much time as possible to have a final design before installation, anticipate all the little things which might come up which are location specific (length of wires needed, type of nails needed for mud wall, etc.)
  The final installation must be “professional”, cannot have a poor “product” just because the poor conditions of the house (i.e. no loose hanging wires, etc.)

## Slide 30: Problems with Evaluating a Design
Balancing between tangible and intangible factors
  A tangible factor is how much the device costs
  An intangible factor is how adopting an idea or device would impact people’s life
  No definite approach to deal with this balance, an approach is to solving it is simply to be as carful as possible to take intangible factors into account when designing

## Slide 31: Problems with Evaluating a Design
The difficulty in making trade-offs, the people who benefit from a design are different from those who lose from it
  Example: the use of chlorofluorocarbons in spray paint benefit the housing and auto industries, but is harmful to the environment
  Example: the use of rare earth elements benefit the electronic industries, but is harmful to the miners and the environment
  Government, sometimes, is not effective in making the trade-offs decision
  The weight of doing justice falls on the designer. The designer need to think carefully about people who might be affected by the decision

## Slide 32: Problems with Evaluating a Design
More examples on the issue of “trade-off” in design
  Environmental Impacts of Automobiles (https://yosemite.epa.gov/r10/owcm.nsf/product+stewardship/autos-impacts)
  “Good product, bad package: top sustainable packaging mistakes” (http://www.theguardian.com/sustainable-business/2014/jul/18/good-product-bad-package-plastic-recycle-mistakes)

## Slide 33: Assignment 4
Three designers were asked to submit proposals for a short-haul (10 miles) transportation system to be built by a community of 100,000. The ridership would be approximately 30,000 trips per day with an average distance of 4 miles. The proposals from the three designers are:
    A subway system
    A bicycle system
    An automobile based system
  List the intangible factors relevant to each of the short-haul transportation system which the design should address
  Consider who, in the long run, might benefit and who might suffer if each of the short-haul transportation systems were implemented. Do the same people tend to benefit and suffer ?